## Slide 1
GEORGE JOSEPH(244102103)
DRASHTI DOSHI(244102102)
A BIDIRECTIONAL BATTERY CHARGER WITH MODULAR
Integrated Charge Equalization Circuit
EE665-Project
1

## Slide 2
Motivation and Objective
  Growing need for high-voltage, reliable EV battery packs and smart charging.
  Need to tackle charge imbalance, battery degradation, and grid integration.
  Achieve power factor correction and low grid current distortion
  Develop and integrate a modular charge equalisation (CEC) algorithm
  Enable bidirectional power flow.
  Enhance battery life and system reliability via modular architecture
2

## Slide 3
Buck/Boost Switching
Dual Loop Controller for Boost H-Bridge switching
Second loop to generate switching pulse
First loop to get ref Current and power
Source
Boost H-Bridge Rectifier (Single switch operation)
Buck/Boost Converter
Battery Stack
Improved PF -> 0.99 (sim.), 0.97 (exp.)
50% reduction of Switching losses
Improved THD -> <3% (sim.), <5% (exp.)
PLL
Genaration of
Iref and Vref
PID Controller
Measured Current and power
Switching logic
PWM pulse through CC mode and CV mode Controller
Batter current ripple reduction -> improves battery life
CEC Control
Reconfig. Battery stack based on SoC of the module
Minimize imbalance

## Slide 4
System Overview
There are three main parts in this circuit
  H-bridge
  DC-DC Converter
  Battery stack
Two modes of operation
  G2V Mode
  V2G Mode

## Slide 5
G2V Mode
Charge the battery from the grid using a controlled current/voltage.
  H-Bridge AC-DC Converter
Here, it acts as a boost rectifier
  Positive Half-Cycle (Vs>0):
    Switches: S12 conducts(Dual loop Control), S22 (body diode conducts).
    Current Path: Vs→S12→L1→Diode of S22→Grid
    Switches: S11, S22(both body diode conducts).
    Current Path: Vs→Diode of S11→L1→Diode of S22→Grid
  Negative Half-Cycle (Vs<0):
    Switches: S22 conducts(Dual loop Control), S21(body diode conducts).
    Current Path: Vs→S12→L1→Diode of S22→Grid
    Switches: S21, S12 (both body diode conducts).
    Current Path: Vs→Diode of S21→L1→Diode of S12→Grid
4
  Buck Converter
  ON State (S31 ON)-Inductor charges
Current Path: Vdc→S31→L3→Battery
  OFF State (S31 OFF)-Inductor discharges
Current Path: Freewheeling diode of S32.

## Slide 6
V2G Mode
1. DC-DC Boost Converter
Discharging the battery
  ON State (S32 ON)-Inductor charges
Current Path: Battery → L3 → S32 → Battery.
  OFF State (S31 OFF)-Inductor discharges
Current Path: Freewheeling diode of S32.
2. DC-AC Inverter
  Positive Half-Cycle (Vs > 0):
Switches: S11 (Dual Loop Control) and S22
Current Path: Vdc → S11→ L1 → Grid → S22
Switches: S21 diode and S11
Current Path: S21diode→ S11 → L1 → Grid
5
Negative Half-Cycle (Vs < 0):
Switches: S21 ,S12 (diode conducts).
Current Path: Vdc → S21 → Grid → L1 → S12 diode
Switches: S21 ,S12 (diode conducts).
Current Path: L2→ S12 → S22 diode → Grid

## Slide 7
CEC
  Balances State-of-Charge (SOC)
  Ensuring that each module charges and discharges uniformly
  Prevents Imbalance and Degradation
  Corrects small differences in capacity or ageing between modules, the CEC prevents overcharging or over-discharging of individual modules
  Enhances Reliability and Flexibility
  Allows faulty modules to be bypassed without interrupting system operation, improving reliability and making maintenance easier
  Improves Battery Life and Usable Capacity
  By maintaining balanced SOC, the CEC extends the overall battery lifespan, maximises usable energy, and supports efficient, safe operation of the EV charger system
6

## Slide 8
CEC Algorithm
V2G Mode (Discharging)
  Activation Order:
    Start with highest SOC module → connect via hip switch.
    Sequentially activate next-highest SOC modules as others deplete.
  Thresholds:
    Connect: If module SOC ≥ average SOC.
    Bypass: If module SOC ≤ average SOC – 5% or drops below 30%.
  Bypass Conditions:
    SOC <30% (prevent over-discharge).
    SOC deviation >5% from average.
  Dynamic Reconfiguration:
    Maintains minimum DC-link voltage (e.g., 400V) by adding/removing modules.
G2V Mode (Charging)
  Activation Order:
    Start with lowest SOC module → connect via hip switch.
    Sequentially activate next-lowest SOC modules as they approach average.
  Thresholds:
    Connect: If module SOC ≤ average SOC.
    Bypass: If module SOC ≥ average SOC + 2% or reaches 100%.
  Bypass Conditions:
    Fully charged (SOC = 100%).
    SOC deviation >2% from average.
  SOC Estimation:
    Coulomb counting + OCV calibration every 60 sec
7

## Slide 9
Control Strategies
8
  Outer Voltage Loop:
    Regulates DC-link voltage (Vdc) to a fixed reference (e.g., 400V) using a PI controller
    Compensates for load variations and ensures stable DC bus voltage for both G2V/V2G modes.
  Inner Current Loop:
    Tracks sinusoidal reference current (iref) synchronized to grid voltage via PLL.
    Minimizes THD (<5%) using PI error correction:
  CC-CV charging in G2V mode:
    Constant Current (CC): Battery charged at fixed current until near full voltage
    Constant Voltage (CV): Voltage held constant, current tapers off as battery reaches full charge
  However this is not typically used in V2G mode
  V2G primarily focuses on discharging energy to the grid, where the goal is to regulate power flow rather than follow a CC-CV profile

## Slide 10
Simulation Parameters
9

## Slide 11
Simulation Diagram
10
Main Circuit
PLL and Reference Generation

## Slide 12
Simulation Diagram
11
Switching Control Logic

## Slide 13
Result
12

## Slide 14
Strengths And Limitations
13

## Slide 15
THANK YOU
14
References
[1] N. Tashakor, E. Farjah, and T. Ghanbari, “A Bidirectional Battery Charger With Modular
Integrated Charge Equalization Circuit,” IEEE Transactions on Power Electronics, vol. 32,
no. 3, pp. 2133–2143, Mar. 2017.